## Slide 1
Real-Time Micro-Climate Solar Telemetry & AI Forecasting System
REVIEW 1 — WEEK 5 PROGRESS
An end-to-end telemetry and deep learning platform built by a three-person engineering team, streaming live micro-climate data, predicting solar wattage output via LSTM, and surfacing automated thermal stress alerts through a live React dashboard.
Project Team & Roles
Mohammed Faiz CK
Full-Stack Developer & System Integrator
Aryan Sovit
AI/ML & Data Pipelines
Yashwanth Chandawat
Data Analytics & Testing
Tech Stack
Frontend
React.js
Backend
Express.js / Node.js
Database
MongoDB
AI / ML
Python — TensorFlow / Keras
Data Source
Open-Meteo API

## Slide 2
The Problem: Solar Output Volatility
Why Existing Systems Fall Short
Rapid Micro-Climate Fluctuation
Solar output fluctuates rapidly due to localised micro-climates and sudden temperature spikes that coarse regional models fail to capture.
Reactive Monitoring Paradigm
Traditional monitoring systems are inherently reactive — they report degradation after it occurs, missing sudden irradiance drops entirely.
No Thermal Stress Visibility
Operators lack real-time visibility into thermal stress and performance degradation, leaving panels exposed to derating risk without automated alerts.
Our Solution
An end-to-end IoT Telemetry platform streaming live weather metrics, predicting wattage output via deep learning (LSTM), and triggering real-time thermal alerts.
Key Value Proposition: Proactive solar forecasting combined with automated thermal stress detection — shifting operators from reactive damage control to predictive performance management.
Live
Real-time telemetry streaming
Predict
LSTM wattage forecasting
Alert
Automated thermal advisories

## Slide 3
Development Timeline & Key Milestones
WEEKS 1 – 5
1
Week 1
Foundation
Requirements gathering, tech stack finalization, MongoDB schema design and environment configuration.
2
Week 2
Telemetry Pipeline
Ingestion script mock_telemetry.py built; Open-Meteo API weather integration operational.
3
Week 3
Deep Learning Model
LSTM Sequence Model architecture defined for 60-step solar wattage prediction. Training pipeline established.
4
Week 4
Backend & APIs
Node.js/Express child-process execution links Python TensorFlow scripts directly to REST endpoints /recent and /predict.
5
Week 5 ✦
Full-Stack UI
Live Recharts visualization, Thermal Advisory Banners, and Anomaly Injection Testing all integrated and operational.
Week 5 marks the first fully integrated end-to-end system run — from sensor ingestion through LSTM inference to live dashboard rendering.

## Slide 4
System Architecture: 5-Step Data Pipeline
Ingestion
Storage
Processing
1
Ingestion
mock_telemetry.py fetches local weather data via Open-Meteo API
2
Storage
MongoDB stores time-series telemetry streams with indexed timestamps
3
Backend Engine
Node.js/Express server spawns Python child processes for model execution
1
AI Processing
predict.py passes a 60-step sequence to the LSTM neural network for wattage inference
2
UI Presentation
React dashboard auto-polls every 5 seconds for continuous Recharts updates

## Slide 5
Live Dashboard Overview
WEEK 5 — UI INTEGRATION COMPLETE
Interactive Telemetry Charts
Animated cubic line charts powered by Recharts display Irradiance vs. Predicted Wattage in real time, auto-refreshing every 5 seconds without page reload.
Live Weather Barometer
Real-time outdoor temperature feed continuously synced with the Open-Meteo API, surfacing ambient conditions relevant to panel efficiency and thermal thresholds.
Quick Audit Export
Single-click CSV export button for client-side reporting and offline data auditing — no backend request required for export generation.
System Status
Live system indicator confirms the dashboard is connected and updating normally.
Dashboard Features in Action

## Slide 6
Anomaly Simulator & System Stress Testing
ENDPOINT: /INJECT-ANOMALY
The anomaly injection framework validates model responsiveness and UI alerting under synthetic but physically realistic stress conditions — confirming that the LSTM and advisory system behave correctly before hardware integration.
☁ Cloud Cover Simulation
Injection: Severe irradiance drop to 120 W/m² triggered via /inject-anomaly
Outcome: Confirms LSTM model immediately revises wattage forecast downward in response to the synthetic irradiance collapse — validating real-time model sensitivity.
🌡 Panel Overheat Simulation
Injection: Synthetic temperature spikes above 40°C pushed into the telemetry stream.
Outcome: Triggers automated UI Advisory Banner warning operators of panel derating and thermal stress — confirming end-to-end alert pipeline integrity.
Advisory banners are suppressed in demo mode. Enable live alerting before field deployment.

## Slide 7
Backend & Machine Learning Deliverables
Integration Architecture
Node.js Child Process Execution
Cross-runtime integration bridging the Express backend directly to Python TensorFlow — without microservice overhead. The server spawns predict.py as a child process, passing telemetry context via stdin and capturing inference output via stdout.
Preprocessing & Normalization
Feature scaling pipeline for irradiance, ambient temperature, and power metrics. All inputs are normalized before being assembled into the 60-step LSTM sequence window.
REST API Suite
/recent
Fetch recent sensor logs from MongoDB time-series store. Used by dashboard on every 5-second poll cycle.
/predict
Execute LSTM inference via Python child process. Returns forecasted wattage for the next sequence window.
/inject-anomaly
Trigger real-world stress scenarios — cloud cover drops or overheat spikes — to validate model and UI advisory response.
60
LSTM Sequence Steps
Input window length for each wattage prediction
5s
Poll Interval
React dashboard auto-refresh rate
3
REST Endpoints
Core API surface powering the full platform
40°C
Thermal Threshold
Temperature level triggering advisory banner

## Slide 8
Future Roadmap & Next Steps
Phase 3 — Cloud Production
Cloud-hosted production deployment and multi-site solar farm management at scale.
Phase 2 — Hardware Integration
Replace synthetic telemetry with real ESP32 & INA219 current/voltage sensors for genuine field data ingestion.
Phase 1 — Mobile Deployment
Deploy via Capacitor / Android Gradle toolchain, enabling field technicians to monitor telemetry and receive thermal alerts on mobile devices.
Where We Are Today
End-to-end system fully integrated through Week 5 — ingestion, LSTM inference, REST API, and live React dashboard all operational with anomaly testing validated.
Open for Questions & Live Demonstration
The system is running live. The team is ready to walk through the dashboard, trigger anomaly injection via /inject-anomaly, and demonstrate LSTM inference in real time.
MOHAMMED FAIZ CK
ARYAN SOVIT
YASHWANTH CHANDAWAT